BIPM TM166 (ftp://tai.bipm.org/TimeLink/LkC/)							1st version: 26 Aug. 2009, Revised: 3 Sep. 2009 and 25 Sept. 2009

Restoration the TWSTFT link calibration using

GPS bridging after the satellite switch from

IS-3R to T-11N in July/August 2009

( around MJD 55043 )

Z. Jiang, W. Lewandowski and D. Piester

Method: We first use the GPS PPP bridge to restore the CALR of the UTC links (LABs-PTB, Table 1 and 3a) then use the Triangle Closure condition (TCC) to compute CALRs of the non-UTC links (LABs-LABs) and then estimate the uncertainty.

For UTC links, the ESDVAR values are kept as they are and for the non-UTC links, there are two cases: for Europe labs: ESDVAR==999999999 (Table 3b) and for NIST and USNO keep their ESDVAR values (Table 3c).

We finally implemented the new CALR values in the TW0909 data (up to 55095) and verified them (Table 4). [3,4] made the independent verifications. There are N(N-1)/2 links, N=9. With the data available, totally 33 new CALR-ESDVAR are computed and listed in Table 3a, 3b, 3c. A brief discussion is given below but for all the details of the method used, c.f. [1,2].

Implementation schedule:

- 55096-55102 (22-28 Sept): The TW LABs check their own CALR and the related ESDVAR in Table 3a, 3b, 3c

- 55102 (28 Sept): The BIPM issues the final version of this TM with the CALR/ESDVAR values and the CI codes

- 55102-55108 (28 Sept - 4 Oct): The TW labs implement the new CALR/ESDVAR and the CI codes in their ITU files (c.f. examples of Header and Recordings below) then upload (re-upload) the corrected ITU files (back up to the satellite switch moment) to the BIPM ftp site for UTC computation. The first MJD of Circular T 262 is 55109.

No data: USNO-ROA, NIST-ROA, USNO-VSL, NPL-LABs, AOS-LABs (a new computation will be made when all the data available)

Data gap ≥ 5 days: IT, OP, SP (c.f. Annex III). This implies the bridge quality might be affected by possible biases in GPS.

References:

[1] TM 151

[2] Jiang, Lewandowski and Piester Proc. PTTI 2008

[3] Report of NIST by Zhang

[4] Report of OP by Rovera and Achkar

Table 1: TW UTC link jumps due to the satellite changes using GPS bridge* (MC/P3/PPP)

(version of 26/8/2009 for the UTC links** with data available on BIPM ftp on 13/8/2009)

| Link | Bridge link | Common Points in period1/period2 | D1±StDev | D2±StDev | Bridge=D1-D2 ± ε *** | Remark |
| --- | --- | --- | --- | --- | --- | --- |
|  | Xband | 61/56 | -3.911±0.403 | -214.916±0.855 | +211.0±0.1 |  |
| USNO-PTB | P3 | 61/67 | -3.396±0.656 | -214.792±0.933 | +211.4±0.1 | Esdvar= -379.910 |
|  | PPP | 61/67 | -2.614±0.372 | -214.149±0.906 | +211.5±0.1 |  |
| NIST-PTB | MC | 62/61 | -0.625±1.212 | 197.639±1.163 | -198.3±0.2 | Rep. Zhang |
|  | PPP | 62/61 | -1.451±0.147 | 195.790±0.230 | -197.2±0.1 | EsdVar=-0.724ns |
| CH-PTB | P3 | 39/101 | -5.142±0.566 | 204.581±0.696 | -209.7±0.2 |  |
|  | PPP | 39/101 | -4.352±0.168 | 205.094±0.408 | -209.5±0.1 |  |
| IT-PTB | P3 | 35/64 | -27.626±0.539 | 452.311±0.717 | -479.9±0.2 |  |
|  | PPP | 35/64 | -29.915±0.407 | 450.212±0.575 | -480.1±0.1 |  |
| OP-PTB | P3 | 51/9 | 1.964±0.618 | 7301.804±0.647 | -7299.9±0.3 | cf. also Rep. Rovera- |
|  | PPP | 51/9 | 1.907±0.192 | 7301.623±0.161 | -7299.9±0.1 | Achkar 21/9/09 |
| ROA-PTB | P3 | 69/68 | -1.480±1.297 | 162.057±1.564 | -298.3±0.2 | EsdVar changed |
|  | PPP | 69/68 | -3.614±0.339 | 159.746±0.972 | -298.1±0.1 | -27.6 to 242.0 |
| SP-PTB | P3 | 61/92 | -2.039±0.907 | 192.406±1.533 | -194.4±0.2 |  |
|  | PPP | 61/92 | -220.489±0.147 | -26.135±0.749 | -194.4±0.1 | Tw gap 55047-55054 |
| VSL-PTB | P3 | 36/98 | -3.131±2.442 | 582.696±0.693 | -585.8±0.4 |  |
|  | PPP | 36/98 | -75.481±2.490 | 510.378±0.550 | -585.9±0.4 | Esdvar= -228.850 |
| NPL-PTB | P3 | 61/0 | 1.216±0.691 | No TW | NA |  |
|  | PPP | 61/0 | 1.344±0.225 | No TW | NA |  |
| AOS-PTB | MC | 228/0 | 2.597±0.916 | No TW | NA |  |

*    Both TW and GPS links should be driven by same clock

**  Only UTC links. BIPM supply the calibration CI and non-UTC TW calibration. BIPM thanks to all the TW colleagues for their full cooperation

*** here ε =±√[(StDev1²+StDev2²)/n]. n is the smaller number of the common points in the period 1 and period 2. ε stands for the statistic uncertainty of the computation. Please note that the possible biases in the GPS links are not taken into account

Period 1 ≈  55039 ~ 55043 (even hours) cf. Annex 1

Period 2 ≈  55043 ~ 55054 (odd hours) cf. Annex 2

D1= link difference: TW(Period 1)-GPS / ns

D2= link difference: TW(Period 2)-GPS / ns

The Bridge=D1-D2 / ns

CALR and estimated uncertainty of the UTC time links

CALRs in Table 2 are taken from bold written bridging results in Table 1.

Uncertainty determination:

new est. uncert. = sqrt [(uncert. before sat. switch)^2+(0.5*combined ESDVAR uncert.)^2+(bridging uncert.)^2]

combined ESDVAR uncert. = sqrt [(ESDVAR uncert. Lab i)^2+(ESDVAR uncert. Lab j)^2]

New CALRs should be reported starting from MJD 55043.

If the ESDVAR should be set to “0” or “999999999” it has to be included in the CALR value.

Table 2:

| Lab i – lab j | CALR (ns) | CI | S | Uncert. Before satellite switch (ns) | ESDVAR uncertainty (ns) Lab i, lab j | Bridging uncertainty (ns) | Uncertainty to be reported in ITU-file header (ns) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| USNO-PTB | +211.5 |  | 1 | 1.1 | 0 | 0.1 | 0.1 | 1.1 |
| NIST-PTB | -197.2 |  | 1 | 5.0 | 0 | 0.1 | 0.1 | 5.0 |
| CH-PTB | -209.5 |  | 1 | 1.0 | 0 | 0 | 0.1 | 1.0 |
| IT-PTB | -480.1 |  | 1 | 1.2 | 0 | 0 | 0.1 | 1.2 |
| OP-PTB | -7299.9 |  | 1 | 1.1 | 0 | 0 | 0.1 | 1.1 |
| ROA-PTB | -298.1 |  | 1 | 5.0 | 0 | 0.1 | 0.1 | 5.0 |
| SP-PTB | -194.4 |  | 1 | 1.0 | 0.5 | 0.1 | 0.2 | 1.1 |
| VSL-PTB | -585.9 |  | 1 | 1.0 | 0.5 | 0.1 | 0.4 | 1.2 |
| AOS-PTB | - |  | 1 | 5.0 | 0 | 0.1 | - |  |
| NPL-PTB | - |  | 1 | 1.2 | 0 | 0 | - |  |

Table 3a CALR/ESDVAR for UTC links

Table 3b CALR for Non-UTC links

Table 3c CALR/ESDVAR for Non-UTC links

Table 4 Verification of the new CALR values with the Triangle closures data of TW0909 (Mjd 55079-55094)

“TW”-file header entries

Here are listed examples to be implemented into the “TW” file header. Because the UTC-links are bridged links the header entry should be “CAL 125 BRIDGED” (see CH01 – PTB01), the non-UTC links are recalibrated by the TCC and thus the header entry should be “TRIANGLE CLOSURE”(see CH01 - IT01).

European “TW”-files:

* LINK   12 SAT: TELSTAR 11N         NLO: E 322 30 00.000  XPNDR: 999999999 ns

*           SAT-NTX: 11004.7200 MHz  SAT-NRX: 14304.7200 MHz  BW:   2.5 MHz

* LINK   13 SAT: TELSTAR 11N         NLO: E 322 30 00.000  XPNDR: 999999999 ns

*           SAT-NTX: 11485.5500 MHz  SAT-NRX: 14026.5500 MHz  BW:   2.5 MHz

US “TW”-files:

* LINK   13 SAT: TELSTAR 11N         NLO: E 322 30 00.000  XPNDR: 999999999 ns

*           SAT-NTX: 11726.5500 MHz  SAT-NRX: 14285.5500 MHz  BW:   2.5 MHz

Examples for the additional header entries:

CH01 – PTB01:

* CAL   139 TYPE: CAL 125 BRIDGED    MJD: 55043  EST. UNCERT.:    1.000 ns

USNO01 – PTB01:

* CAL   140 TYPE: CAL 114 BRIDGED    MJD: 55043  EST. UNCERT.:    1.100 ns

NIST01 – PTB01:

* CAL   141 TYPE: CAL 113 BRIDGED    MJD: 55043  EST. UNCERT.:    5.000 ns

IT01 – PTB01:

* CAL   142 TYPE: CAL 113 BRIDGED    MJD: 55043  EST. UNCERT.:    1.200 ns

OP01 – PTB01:

* CAL   143 TYPE: CAL 134 BRIDGED    MJD: 55043  EST. UNCERT.:    1.100 ns

ROA01 – PTB01:

* CAL   144 TYPE: CAL 118 BRIDGED    MJD: 55043  EST. UNCERT.:    5.000 ns

SP01 – PTB01:

* CAL   145 TYPE: CAL 119 BRIDGED    MJD: 55043  EST. UNCERT.:    1.100 ns

VSL01 – PTB01:

* CAL   146 TYPE: CAL 120 BRIDGED    MJD: 55043  EST. UNCERT.:    1.200 ns

CH01 – IT01:

* CAL   147 TYPE: TRIANGLE CLOSURE   MJD: 55043  EST. UNCERT.:    2.000 ns

Examples for ITU-format data recordings

Examples for the data lines are listed in the following. Changes to be applied are in bold and red numbers.

* EARTH-STAT  LI  MJD  STTIME NTL        TW        DRMS SMP ATL     REFDELAY     RSIG  CI S    CALR     ESDVAR   ESIG TMP HUM PRES

* LOC    REM           hhmmss  s         s          ns       s         s          ns            ns        ns      ns degC  %  mbar

currently:

CH01  PTB01 12 55097 013700 119  0.265074502392 1.237 119 118  0.000000753388 0.600 999 9 999999999 999999999 99999 999 999 9999

PTB01   CH01 12 55097 013700 119  0.265074616809 2.097 120 119  0.000000489403 0.010 999 9 999999999 999999999 99999  12  96 1011

recalibrated:

CH01  PTB01 12 55097 013700 119  0.265074502392 1.237 119 118  0.000000753388 0.600 139 1  -209.500 999999999 99999 999 999 9999

PTB01   CH01 12 55097 013700 119  0.265074616809 2.097 120 119  0.000000489403 0.010 139 1   209.500 999999999 99999  12  96 1011

currently:

USNO01  PTB01 04 55097 014600 119  0.262380586649 0.570 119 118  0.000000859104 99999 114 1   218.800  -379.910 99999 433 100 1019

PTB01 USNO01 13 55097 014600 119  0.262381400965 0.231 120 119  0.000000489323 0.009 999 9 999999999 999999999 99999  13  93 1012

recalibrated:

USNO01  PTB01 13 55097 014600 119  0.262380586649 0.570 119 118  0.000000859104 99999 140 1   211.500  -379.910 99999 433 100 1019

PTB01 USNO01 13 55097 014600 119  0.262381400965 0.231 120 119  0.000000489323 0.009 140 1  -211.500 999999999 99999  13  93 1012

currently:

NIST01  PTB04 11 55042 024900 119 +0.268973263627 0.228 120 119 +0.000000858900 99999 113 1   -30.100 -00000.720 0.500  13  92  840

PTB04 NIST01 11 55042 004900 119  0.268949641927 0.217 120 119  0.000000511955 0.012 113 1    30.100    -0.180 0.100  18  71 1000

recalibrated:

NIST01  PTB01 13 55042 024900 119 +0.268973263627 0.228 120 119 +0.000000858900 99999 141 1  -197.200    -0.720 0.500  13  92  840

PTB01 NIST01 13 55042 004900 119  0.268949641927 0.217 120 119  0.000000511955 0.012 141 1   197.200 999999999 99999  18  71 1000

currently:

IT02  PTB01 12 55097 011300 119 +0.264679735451 1.707 119 119 +0.000044060184 0.500 999 9 999999999 999999999 99999  16 062 0999

PTB01   IT02 12 55097 011300 119  0.264765946380 0.870 119 119  0.000000489431 0.012 999 9 999999999 999999999 99999  13  91 1012

recalibrated:

IT02  PTB01 12 55097 011300 119 +0.264679735451 1.707 119 119 +0.000044060184 0.500 142 1  -480.100 999999999 99999  16 062 0999

PTB01   IT02 12 55097 011300 119  0.264765946380 0.870 119 119  0.000000489431 0.012 142 1   480.100 999999999 99999  13  91 1012

currently:

OP01  PTB04 12 55097 011900 119  0.264560877946 1.226 120 119  0.000017420050 0.050 999 9 99999.999 99999.999 9.999 +17  69 1020

PTB01   OP01 12 55097 011900 119  0.264580122406 1.166 120 119  0.000000489427 0.012 999 9 999999999 999999999 99999  13  95 1012

recalibrated:

OP01  PTB01 12 55097 011900 119  0.264560877946 1.226 120 119  0.000017420050 0.050 143 1 -7299.900 999999999 99999 +17  69 1020

PTB01   OP01 12 55097 011900 119  0.264580122406 1.166 120 119  0.000000489427 0.012 143 1  7299.900 999999999 99999  13  95 1012

currently:

ROA01  PTB01 12 55097 011600 119 +0.260354631483 1.524 117 117 +0.000000802861 0.050 118 1  -288.400  +242.000 99999 +20  53 1014

PTB01  ROA02 12 55097 011600 119  0.260354966824 0.539 120 119  0.000000489473 0.011 999 9 999999999 999999999 99999  13  95 1012

recalibrated:

ROA01  PTB01 12 55097 011600 119 +0.260354631483 1.524 117 117 +0.000000802861 0.050 144 1  -298.100  +242.000 99999 +20  53 1014

PTB01  ROA02 12 55097 011600 119  0.260354966824 0.539 120 119  0.000000489473 0.011 144 1   298.100 999999999 99999  13  95 1012

currently:

SP01  PTB01 12 55096 012800 119 +0.268275209693 2.238 117 119 +0.000000823017 0.050 999 9 99999.999 99999.999 9.999 999 999 9999

PTB01   SP01 12 55096 012800 119  0.268275490476 0.988 120 119  0.000000490972 0.017 999 9 999999999 999999999 99999  10  98 1014

recalibrated:

SP01  PTB01 12 55096 012800 119 +0.268275209693 2.238 117 119 +0.000000823017 0.050 145 1  -194.400 999999999 99999 999 999 9999

PTB01   SP01 12 55096 012800 119  0.268275490476 0.988 120 119  0.000000490972 0.017 145 1   194.400 999999999 99999  10  98 1014

currently:

VSL01  PTB04 12 55097 092500 119 +0.265572936428 0.753 114 119 +0.000000709411 0.050 999 0 +9999.999  +228.850 0.500 +17  82 1021

PTB01  VSL01 12 55097 092500 119  0.265572470636 1.473 120 119  0.000000488028 0.010 999 9 999999999 999999999 99999  16  88 1013

recalibrated:

VSL01  PTB04 12 55097 092500 119 +0.265572936428 0.753 114 119 +0.000000709411 0.050 146 1  -585.900  +228.850 0.500 +17  82 1021

PTB01  VSL01 12 55097 092500 119  0.265572470636 1.473 120 119  0.000000488028 0.010 146 1   585.900 999999999 99999  16  88 1013

currently:

CH01   IT02 12 55097 014300 119  0.263105317768 0.505 120 119  0.000000753332 0.600 999 9 999999999 999999999 99999 999 999 9999

IT02   CH01 12 55097 014300 119 +0.263019218006 2.618 119 119 +0.000044060184 0.500 999 9 999999999 999999999 99999  16 062 0999

recalibrated:

CH01   IT02 12 55097 014300 119  0.263105317768 0.505 120 119  0.000000753332 0.600 147 1   268.499 999999999 99999 999 999 9999

IT02   CH01 12 55097 014300 119 +0.263019218006 2.618 119 119 +0.000044060184 0.500 147 1  -268.499 999999999 99999  16 062 0999

Annex I

Time link differences of period 1

(even hours before 55043)

TW-GPS

TW-GPS MC (LAB2-LAB1.TGTM5)

TW-GPS P3 (LAB2-LAB1.TGTA5)

TW-GPS PPP (LAB2-LAB1.TGT35)

Annex II

Time link differences of period 2

(odd hours after 55043)

TW-GPS

TW-GPS MC (LAB2-LAB1.TGTM5)

TW-GPS P3 (LAB2-LAB1.TGTA5)

TW-GPS PPP (LAB2-LAB1.TGT35)

Annex III

UTC TW Time links using the new CALR/ESDVAR values in Table 3a

# Text boxes

CI   S   LABi LABj   CALR/ns  U/ns   ESDVAR/ns

139   1   PTB   CH    209.500   1.0   999999999

1    CH  PTB   -209.500   1.0   999999999

140   1   PTB USNO   -211.500   1.1   999999999

1  USNO  PTB    211.500   1.1    -379.910

141   1   PTB NIST    197.200   5.0   999999999

1  NIST  PTB   -197.200   5.0      -0.724

142   1   PTB   IT    480.100   1.2   999999999

1    IT  PTB   -480.100   1.2   999999999

143   1   PTB   OP   7299.900   1.1   999999999

1    OP  PTB  -7299.900   1.1   999999999

144   1   PTB  ROA    298.100   5.0   999999999

1   ROA  PTB   -298.100   5.0     242.000

145   1   PTB   SP    194.400   1.1   999999999

1    SP  PTB   -194.400   1.1   999999999

146   1   PTB  VSL    585.900   1.2   999999999

1   VSL  PTB   -585.900   1.2     228.850

TYPE: G.B. (GPS bridge)

Used Since: 30 Sept. 2009

Remark: TM166

CI   S  LABi LABj    CALR/ns  U/ns   ESDVAR/ns

162   1  USNO   CH    422.290   2.0    -379.910

1    CH USNO   -422.290   2.0   999999999

163   1  USNO   IT    687.732   2.0    -379.910

1    IT USNO   -687.732   2.0   999999999

164   1  USNO   OP   7512.354   2.0    -379.910

1    OP USNO  -7512.354   2.0   999999999

165   1  USNO   SP    406.671   2.0    -379.910

1    SP USNO   -406.671   2.0   999999999

166   1  NIST   CH     11.859   6.0      -0.724

1    CH NIST    -11.859   6.0   999999999

167   1  NIST   IT    280.069   6.0      -0.724

1    IT NIST   -280.069   6.0   999999999

168   1  NIST   OP   7102.736   6.0      -0.724

1    OP NIST  -7102.736   6.0   999999999

169   1  NIST   SP     -3.680   6.0      -0.724

1    SP NIST      3.680   6.0   999999999

170   1  NIST  VSL    273.418   6.0      -0.724

1   VSL NIST   -273.418   6.0   999999999

TYPE: T.C. (triangle closure)

Used Since: 30 Sept. 2009

Remark: TM166

CI  S   LABi LABj    CALR/ns  U/ns  ESDVAR/ns

147  1     CH   IT    268.499   2.0  999999999

1     IT   CH   -268.499   2.0  999999999

148  1     CH   OP   7091.614   2.0  999999999

1     OP   CH  -7091.614   2.0  999999999

149  1     CH  ROA    -30.460   6.0  999999999

1    ROA   CH     30.460   6.0  999999999

150  1     CH   SP    -14.027   2.0  999999999

1     SP   CH     14.027   2.0  999999999

151  1     CH  VSL    262.637   2.0  999999999

1    VSL   CH   -262.637   2.0  999999999

152  1     IT   OP   6820.466   2.0  999999999

1     OP   IT  -6820.466   2.0  999999999

153  1     IT  ROA   -302.867   6.0  999999999

1    ROA   IT    302.867   6.0  999999999

154  1     IT   SP   -284.760   2.0  999999999

1     SP   IT    284.760   2.0  999999999

155  1     IT  VSL     -8.265   2.0  999999999

1    VSL   IT      8.265   2.0  999999999

156  1     OP  ROA  -7121.489   6.0  999999999

1    ROA   OP   7121.489   6.0  999999999

157  1     OP   SP  -7105.712   2.0  999999999

1     SP   OP   7105.712   2.0  999999999

158  1     OP  VSL  -6828.525   2.0  999999999

1    VSL   OP   6828.525   2.0  999999999

159  1    ROA   SP     16.066   6.0  999999999

1     SP  ROA    -16.066   6.0  999999999

160  1    ROA  VSL    293.982   6.0  999999999

1    VSL  ROA   -293.982   6.0  999999999

161  1     SP  VSL    276.616   2.0  999999999

1    VSL   SP   -276.616   2.0  999999999

TYPE: T.C. (triangle closure)

Used Since: 30 Sept. 2009

Remark: TM166

Labi Labj        CARL+/-StDev     N  ESIG

CH   IT     -0.092 +/- 0.405,  194 0.029

IT   CH      0.092 +/- 0.405,  194 0.029

CH NIST     -0.413 +/- 0.256,  169 0.020

NIST   CH      0.413 +/- 0.256,  169 0.020

CH   OP     -0.216 +/- 0.543,  167 0.042

OP   CH      0.216 +/- 0.543,  167 0.042

CH  ROA      NaN   +/-NaN  ,     0-NaN

ROA   CH      NaN   +/-NaN  ,     0-NaN

CH   SP     -0.150 +/- 0.553,  168 0.043

SP   CH      0.150 +/- 0.553,  168 0.043

CH USNO      0.113 +/- 0.353,  163 0.028

USNO   CH     -0.113 +/- 0.353,  163 0.028

CH  VSL     -0.337 +/- 1.122,  122 0.102

VSL   CH      0.337 +/- 1.122,  122 0.102

IT NIST     -0.188 +/- 0.479,  173 0.036

NIST   IT      0.188 +/- 0.479,  173 0.036

IT   OP     -0.267 +/- 0.466,  166 0.036

OP   IT      0.267 +/- 0.466,  166 0.036

IT  ROA      NaN   +/-NaN  ,     0-NaN

ROA   IT      NaN   +/-NaN  ,     0-NaN

IT   SP     -0.087 +/- 0.412,  167 0.032

SP   IT      0.087 +/- 0.412,  167 0.032

IT USNO     -0.611 +/- 0.810,  171 0.062

USNO   IT      0.611 +/- 0.810,  171 0.062

IT  VSL     -0.371 +/- 0.519,  128 0.046

VSL   IT      0.371 +/- 0.519,  128 0.046

NIST   OP      0.262 +/- 0.453,  170 0.035

OP NIST     -0.262 +/- 0.453,  170 0.035

NIST   SP      0.402 +/- 0.468,  171 0.036

SP NIST     -0.402 +/- 0.468,  171 0.036

NIST  VSL      0.081 +/- 0.880,  141 0.074

VSL NIST     -0.081 +/- 0.880,  141 0.074

OP  ROA      NaN   +/-NaN  ,     0-NaN

ROA   OP      NaN   +/-NaN  ,     0-NaN

OP   SP      0.139 +/- 0.365,  171 0.028

SP   OP     -0.139 +/- 0.365,  171 0.028

OP USNO      0.209 +/- 0.454,  167 0.035

USNO   OP     -0.209 +/- 0.454,  167 0.035

OP  VSL      0.012 +/- 0.602,  128 0.053

VSL   OP     -0.012 +/- 0.602,  128 0.053

ROA   SP      NaN   +/-NaN  ,     0-NaN

SP  ROA      NaN   +/-NaN  ,     0-NaN

ROA  VSL      NaN   +/-NaN  ,     0-NaN

VSL  ROA      NaN   +/-NaN  ,     0-NaN

SP USNO      0.251 +/- 0.503,  166 0.039

USNO   SP     -0.251 +/- 0.503,  166 0.039

SP  VSL      0.005 +/- 0.573,  128 0.051

VSL   SP     -0.005 +/- 0.573,  128 0.051